## Slide 1: SHALE-OIL PRODUCTION RESILIENCE and ASSOCIATED SHALE-OIL RESERVES : A GLOBAL APPROACH based on THE PETROLEUM SYSTEM
Marc BLAIZOT, June the 13th, 2017.
marc.blaizot@laposte.net

## Slide 2: Presentation Highlights
Introduction : LTO Resilience ?
Oil retention and Global LTO Resources
Oil recovery and Global LTO Reserves
Conclusions : Where to go and for how long ?
LTO Definition follows D. Jarvie [2012] stating that “shale-oil is oil stored in organic rich intervals (the source rock itself) or migrated into juxtaposed organic lean intervals”.

## Slide 3
Chart: 
from US-EIA, April 2017, Bakken drilling productivity Report
Recent (2016) and unexpected Bakken LTO Production Resilience
In Kbopd

## Slide 4: Presentation Highlights
Introduction : LTO Resilience ?
Oil retention and Global LTO Resources
Oil recovery and Global LTO Reserves
Conclusions : Where to go and for how long ?
LTO Definition follows D. Jarvie [2012] stating that “shale-oil is oil stored in organic rich intervals (the source rock itself) or migrated into juxtaposed organic lean intervals”.

## Slide 5: OIL Trapped in shale-oil : How much ? From P.K. MEYER, O&G Journal, May 2012
80% trapped in SR!!!, 2% trapped in Conventional Reservoir ; 18% lost in migration ;
RF : 7% in SR , 35% in CR

## Slide 6
* AFTER W. ENGLAND, AAPG MEMOIR 60, 1994
OUR “CLASSICAL PETROLEUM SYSTEM ASSUMPTIONS” : NO RETENTION ?
PSY = HCA / HCG
PSY is OK but WHERE IS THE RETENTION WITHIN SOURCE ROCK ?

## Slide 7
WHAT ARE INDICATING LAB MEASUREMENTS IN SOURCE-ROCKS?
Before Expulsion starts, sufficient hydrocarbons quantities have to be generated to saturate the kerogen porosity.
This amount is the Minimum Transformation Ratio to get Expulsion. This minimum could be also the maximum retention peak ?
Maximum values of hydrocarbon (S1) around 250g/gTOC ( Jarvie, AAPG 2012 in several SO in the USA)
And Hydrocarbon present are around 35 %of initial potential
from . ESPITALIE and E. LAFARGUE, 12/1996

## Slide 8: PSY VALUES FOR MATURE BASINS : PSY average : 5% but in EHO Belts (Orinoco, ALBERTA) : 50%
Modified From JJ Biteau et al. , First Break , EAGE, November 2010
Are EHO Belts migration products, good proxy for migration products lost in other basins ?

## Slide 9: A GLOBAL APPROACH TO RETENTION in SOURCE ROCKS
Generation
7500/0.05 = 150000 Gb
Migration
Dismigration and losses
Conventional OOIP
3000/0.4 = 7500 Gb
OIP Retention in SR
150000/2 = 75000 Gb
PSY = 5%
Migration Loss = 45%
50 %
50 %
45 %
5%

## Slide 10: Presentation Highlights
Introduction : LTO Resilience ?
Oil retention and Global LTO Resources
Oil recovery and Global LTO Reserves
Conclusions : Where to go and for how long ?
LTO Definition follows D. Jarvie [2012] stating that “shale-oil is oil stored in organic rich intervals (the source rock itself) or migrated into juxtaposed organic lean intervals”.

## Slide 11
POROSITY WITHIN SHALES (Upper Cretaceous Eagle Ford Example)
Organic Porosity increasing with maturity !
TOC: 1.5 % in weight
TOC : 3% in volume
Organic Porosity :4 to 6%
Oil mainly adsorbed at or absorbed within Kerogen : high HC-wettability
Organic porosity is oil bearing
adapted from H. Cander (bp) , AAPG Annual Convention,April 2012

## Slide 12: Oil SATURATION in SHALE OILS : the Bakken Example (1)
In the Bakken Shales
(Carboniferous/Devonian)
Water cuts in vertical wells drilled
and produced in the 80’s
= before hydraulic fracking
were very low (few %)
supporting a high So ;
Geochemical and petrophysical
studies invoke always
a hydrocarbon wet « reservoir »
Production table from L Price and J LeFever , USGS, 1992

## Slide 13
OIL SATURATION in SHALE OILS : The Bakken example (2)
Last drilled horizontal wells in Bakken show an increasing Water Cut for newer wells, from 20% (2008/2009) to 45 % (2012/2013)
Water Cut is a good indicator of the whole SR depletion and decreasing oil saturation (or increasing water venues through fractures)
But Water cuts are more stable with wells ages than previously thought
From http://fractionalflow.com post by Rune Likvern on December 2014

## Slide 14: From Global LTO ressources to reserves
Assuming a 10 % Recovery Factor : 75000/10 = 7500 Gbo
Assuming a 20 % « acceptability » surface : 7500/5 = 1500 Gb
RF : Geology and geomechanics but also finances (100 $/b)
Acceptability : geography, environment, societal limitations

## Slide 15: US-EIA 2013 Studies : 335 Gbo

## Slide 16: 335 GB of SHALE OILS RECOVERABLES RESERVES (EIA Reports, 2013) SEEMS to be DEEPLY UNDERESTIMATED
Only 137 SO formations in only 95 Onshore Basins considered
  All Middle East and Caspian basins excluded !
  Low quality (not really defined) areas are… discarded ;
  Light HC included in shales gas not in shales oil!
OOIP is Risked ; Risk factor is comprised between 60 % (Vaca Muerta) and 12 % (Parana) ; classical values : 20% (ex :Timimoun, Ahnet )
RF are low : between 2-4 % up to 6-8 % mainly based upon TOC (+ 2%) , Clay Content (Less than ?), Formation pressure (above Hydrostatics), moderate geological complexity (faulting)

## Slide 17: Presentation Highlights
Introduction : LTO Resilience ?
Oil retention and Global LTO Resources
Oil recovery and Global LTO Reserves
Conclusions : Where to go and for how long ?
LTO Definition follows D. Jarvie [2012] stating that “shale-oil is oil stored in organic rich intervals (the source rock itself) or migrated into juxtaposed organic lean intervals”.

## Slide 18
Onshore sag and foreland basins with large type II transgressive SR seem the best candidates, excluding type III SR bearing deltaïc basins,
They correspond mainly to low faulted and pressured parts of horizontally drained basins according to Perrodon (1995).
Conclusion (1) : Where shale we look for ?

## Slide 19
Daily oil production (Mbopd)
2025
2037
Without new LTO
With new 1500 Gbo LTO at 100 $/b,
Conclusion (2) : For how long ?